## Slide 1
Lecture 06: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: Sequential Circuits
Sequential Logic:
  Output depends not only on current input but also on past input values
  Store information between operations (no need for cascading)
  Need some type of memory to remember the past input values
Combinational Logic:
  Output depends only on current input
  Able to perform useful operations (add/subtract/multiply/…)
  Require cascading of many structures
  Costly and inflexible

## Slide 3: Sequential Circuits (cont.)
Circuits that we
have learned
so far
Information Storing
Circuits
Timed “States”

## Slide 4: Sequential Logic: Concept
Sequential Logic circuits remember past inputs and past circuit state.
Outputs from the system are “fed back” as new inputs (usually with delay).
The storage elements are circuits that are capable of storing binary information: memory.

## Slide 5: Synchronous vs. Asynchronous machines
There are two types of sequential circuits:
Synchronous (latch mode) sequential circuit: the behavior can be defined from knowledge of its signal at discrete instants of time. This type of circuits achieves synchronization by using a timing signal called the clock.
Asynchronous (fundamental mode) sequential circuit: the behavior is dependent on the order of input signal changes over continuous time, and output can change at any time (clockless).

## Slide 6: Clock Signal
Different duty cycles
Clock generator: Periodic train of clock pulses

## Slide 7: Synchronous Sequential Circuits: Flip flops as state memory
The flip-flops receive their inputs from the combinational circuit and also from a clock signal with pulses at fixed intervals of time, as shown in the timing diagram.

## Slide 8: SR Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
0
1
1
0
1 0 Set
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND

## Slide 9: SR Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
1
1
0
1 0 Hold
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
1 0 Set

## Slide 10: SR Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
0
0
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
1 0 Hold
1 0 Set
0 1 Reset

## Slide 11: SR Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
1
1
0
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
0 1 Hold
1 0 Set
0 1 Reset
1 0 Hold

## Slide 12: SR Latch (NAND version)
S’
R’
Q
Q’
0 0
0 1
1 0
1 1
S’ R’ Q Q’
0
0
1
1
0 0 1
0 1 1
1 0 1
1 1 0
X Y NAND
0 1 Hold
1 0 Set
0 1 Reset
1 0 Hold
1 1 Invalid

## Slide 13: SR Latch (NOR version)
S’
R’
Q
Q’
0
0
1
0
0
1
1
1
0/1 1/0
0
1
1
0
0
0
(a) Circuit
(b) Truth table
Q
Q’
S’
R’
(no change)
x1 | x2 | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR Gate Truth table
(invalid)

## Slide 14: SR Latch with Enable signal (Gated SR Latch)
S’
R’
Q
Q’
S
R
EN
S R EN S’ R’ Q Q’
0 0 1 1 1 Q0 Q0’ Store
0 1 1 1 0 0 1 Reset
1 0 1 0 1 1 0 Set
1 1 1 0 0 1 1 Disallowed
X X 0 1 1 Q0 Q0’ Store
Latch is sensitive to input changes ONLY when EN=1

## Slide 15: SR Latch with Enable signal (cont.)

## Slide 16: Flip-Flops
Latches are “transparent” (= any change on the inputs is seen at the outputs immediately).
This causes synchronization problems!
Solution: use latches to create flip-flops that can respond (update) ONLY on SPECIFIC times (instead of ANY time).

## Slide 17: Alternatives in FF choice
Type of FF
  SR
  D
  JK
Type of triggering
  Untriggered (asynchronous)
  Level-triggered (EN = 1)
  Edge-triggered (rising or falling edge of CLK)

## Slide 18: Edged-Triggered SR FF

## Slide 19: D Latch
Ensures S and R inputs never equal to 1 at the same time
Useful in control application where setting or resetting a flag to some condition is needed
Stores bits of information
Constructed from a gated SR latch and a Data latch This is done in the D latch:
EN

## Slide 20: D Latch (cont.)
S R CLK Q Q’
0 0 1 Q0 Q0’ Store
0 1 1 0 1 Reset
1 0 1 1 0 Set
1 1 1 1 1 Disallowed
X X 0 Q0 Q0’ Store
0 1 0 1
1 1 1 0
X 0 Q0 Q0’
D CLK Q Q’

## Slide 21: D latch: store it and look it up
Output depends on clock
  Clock high: Input passes to output
  Clock low: Latch holds its output
Latches are level sensitive and “transparent”
D
Q
Q
CLK
Input
Output
Output
CLK
D
Qlatch

## Slide 22: D flip-flop
Input sampled at clock edge
  Rising edge: Input passes to output
  Otherwise: Flip-flop holds its output
Flip-flops can be rising-edge triggered or falling-edge triggered
D
Q
Q
CLK
Input
Output
Output
CLK
D
Qff

## Slide 23: Flip-Flop Vs. Latch
The primary difference between a D flip-flop and D latch is the EN/CLOCK input.
The flip-flop’s CLOCK input is edge sensitive, meaning the flip-flop’s output changes on the edge (rising or falling) of the CLOCK input.
The latch’s EN input is level sensitive, meaning the latch’s output changes on the level (high or low) of the EN input.
Notes: This slide details the primary difference between the often confused D flip-flop and D latch.

## Slide 24: Flip-Flop Vs. Latch (cont.)
behavior is the same unless input
changes while the clock is high
CLK
D
Qff
Qlatch
D
Q
Q
CLK
D
Q
Q
CLK

## Slide 25: Clock Edges
1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Positive Edge Transition
Negative Edge Transition

## Slide 26: PGT & NGT
CLK
D
Q
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
 : Rising Edge of Clock |  |  | 
D | CLK |  | 
0 |  | 0 | 1
1 |  | 1 | 0
 : Falling Edge of Clock |  |  | 
CLK
D
Q
Positive-Going Transition (PGT) Trigger
Negative-Going Transition (PGT) Trigger
Notes: Schematic symbol and excitation table for the positive edge triggered and negative edge triggered D flip-flops

## Slide 27: Flip-Flop Timing
Synchronous control input | 1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | tS Setup Time |  |  |  |  |  |  |  |  | tH Hold Time |  |  | 
Positive Edge Clock | 1 0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Setup Time (tS): The time interval before the active transition of the clock signal during which the synchronous input must be maintained.
Hold Time (tH): The time interval after the active transition of the clock signal during which the synchronous input must be maintained.
Notes: Definition of the Setup & Hold Time timing parameters for a flip-flop.

## Slide 28: Asynchronous Inputs
PR PRESET | CLR CLEAR | CLK CLOCK | D DATA |  |  | 
1 | 1 |  | 0 | 0 | 1 | 
1 | 1 |  | 1 | 1 | 0 | 
0 | 1 | X | X | 1 | 0 | Asynchronous Preset
1 | 0 | X | X | 0 | 1 | Asynchronous Clear
0 | 0 | X | X | 1 | 1 | ILLEGAL CONDITION
CLK
D
Q
PR
CLR
Asynchronous inputs (Preset & Clear) are used to override the clock/data inputs and force the outputs to a predefined state.
The Preset (PR) input forces the output to:
The Clear (CLR) input forces the output to:
Notes: Definition for the PR (preset) and CLR (clear) Asynchronous input for a D flip-flop.

## Slide 29: D Flip-Flop: PR & CLR Timing
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Q=1
Preset
Q=D=0
Clocked
Q=D=0
Clocked
Q=1
Preset
Q=D=0
Clocked
Q=0
Clear
Q=D=1
Clocked
Q=D=1
Clocked
Q=D=1
Clocked
Notes: Time diagram showing the effects of the synchronous inputs (D & CLK) and asynchronous inputs (PR & CLR).

## Slide 30: JK-FF
Widely used type of flip-flop.
The functioning is identical to that of the SR-FF in the SET, RESET, and NO CHANGE.
  The difference is that the JK-FF has NO invalid state as does the SR-FF.
J | K | CLK | Q | 
0 | 0 |  |  | No Change
0 | 1 |  | 0 | Clear
1 | 0 |  | 1 | Set
1 | 1 |  |  | Toggle
 : Rising Edge of Clock |  |  |  | 
K
J
Q
CLK

## Slide 31: JK Flip-Flop: Timing Diagram
Q |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
K |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CLK |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SET
CLEAR
TOGGLE
NO
CHANGE
TOGGLE
NO
CHANGE
SET
Notes: Timing diagram example for a J/K flip-flop.

## Slide 32
T Flip-Flop
If T=0 then it stays in its current state
If T=1 then it reverses its current state

## Slide 33
T-FF using D-FF & JK-FF
T
D
Q
Q
Clock
J
Q
Q
K
T
Clock

## Slide 34
End