## Slide 1
Lecture 09: Digital System Design
Dept. of Computer Sc. and Engg.
University of Rajshahi
www.ru.ac.bd
Dr. Mahboob Qaosar

## Slide 2: Evolution of Computer-Aided Digital Design
SSI: Small scale integration
  A few gates on a chip
MSI: Medium scale integration
  Hundreds of gates on a chip
LSI: Large scale integration
  Thousands of gates on a chip
  CAD: Computer-Aided Design
    CAD vs. CAE
  Logic and circuit simulators
  Prototyping on bread board
  Layout by hand (on paper or a computer terminal)

## Slide 3: Evolution of Computer-Aided Digital Design (cont’d)
VLSI: Very Large Scale Integration
  Hundred thousands of gates
  Not feasible anymore:
    Bread boarding
    Manual layout design
  Simulator programs
  Automatic place-and-route
  Bottom-Up design
    Design small building blocks
    Combine them to develop bigger ones
  More and more emphasis on logic simulation

## Slide 4: HDL: Hardware Description Language
HDL is designed for circuit verification and simulation, for timing analysis, for test analysis (testability analysis and fault grading) and for logic synthesis.
  before you get to the structural level of your design, you want to make sure the logical paths of your design is faultless and meets the spec.
HDLs allowed the designers to model the concurrency of processes found in hardware elements.
The Digital circuits could be described at a register transfer level (RTL) by using HDL.
Used for simulation of system boards; interconnect buses, FPGAs (Field Programmable Gate Arrays), and PALs (Programmable Array Logic).
Example: Verilog HDL, VHDL

## Slide 5
Behavioral description
RTL description (HDL)
Functional verification and testing
Logic synthesis/timing verification
Gate-Level Netlist
Logic verification and testing
Floor planning Automatic place and Route
Physical layout
Layout verification
Implementation
Design specification
HDL Design Flow

## Slide 6: Importance of HDLs
Retargeting to a new fabrication technology
Functional verification earlier in the design cycle
Textual concise representation of the design
  Similar to computer programs
  Easier to understand

## Slide 7: Popularity of Verilog HDL
Verilog HDL
  General-purpose
  Easy to learn, easy to use
  Similar in syntax to C
  Allows different levels of abstraction and mixing them
  Supported by most popular logic synthesis tools
  Post-logic-synthesis simulation libraries by all fabrication vendors
  PLI to customize Verilog simulators to designers’ needs

## Slide 8: Trends in HDLs
Design at behavioral level
Formal verification techniques
Very high speed and time critical circuits
  e.g. microprocessors
  Mixed gate-level and RTL designs
Hardware-Software Co-design
  System-level languages: SystemC, SpecC, …

## Slide 9: Basics of Digital Design Using HDLs
Circuit Under Design (CUD)
8
4
Generating inputs to CUD
Checking outputs of CUD
Test bench
Stimulus block

## Slide 10: Verilog Basic Building Block
Module
  module not_gate(in, out); // module name+ports
  // comments: declaring port type
  input in;
  output out;
  // Defining circuit functionality
  assign out = ~in;
  endmodule

## Slide 11: Hierarchical Modeling Concepts
Top Level
Module
Sub-Module
1
Sub-Module
2
Basic Module
3
Basic Module
2
Basic Module
1
Full Adder
Half Adder
Half Adder
E.g.

## Slide 12: Design Methodologies

## Slide 13: 4-bit Ripple Carry Counter

## Slide 14: T-flipflop and the Hierarchy

## Slide 15: Modules
  module <module_name>(<module_terminal_list>);
  ...
  <module internals>
  ...
  endmodule
Example:
  module T_ff(q, clock, reset);
  ...
  <functionality of T_flipflop>
  ...
  endmodule

## Slide 16: Modules (cont’d)
Verilog supported levels of abstraction
  Behavioral (algorithmic) level
    Describe the algorithm used
    Very similar to C programming
  Dataflow level
    Describe how data flows between registers and is processed
  Gate level
    Interconnect logic gates
  Switch level
    Interconnect transistors (MOS transistors)

## Slide 17: Instance
A module provides a template which you can create actual objects.
When a module is invoked, Verilog creates a unique object from the template
The process of creating a object from module template is called instantiation
The object is called instance

## Slide 18: Instances
module ripple_carry_counter(q, clk, reset);
output [3:0] q;
input clk, reset;
//4 instances of the module TFF are created.
TFF tff0(q[0],clk, reset);
TFF tff1(q[1],q[0], reset);
TFF tff2(q[2],q[1], reset);
TFF tff3(q[3],q[2], reset);
endmodule

## Slide 19: Instances (cont’d)
module TFF(q, clk, reset);
output q;
input clk, reset;
wire d;
DFF dff0(q, d, clk, reset);
not n1(d, q); // not is a Verilog provided primitive.
endmodule
// module DFF with asynchronous reset
module DFF(q, d, clk, reset);
output q;
input d, clk, reset;
reg q;
always @(posedge reset or negedge clk)
if (reset)
q = 1'b0;
else
q = d;
endmodule

## Slide 20: Instances (cont’d)
Illegal instantiation example:
  Nested module definition not allowed
  Note the difference between module definition and module instantiation
// Define the top level module called ripple carry
// counter. It is illegal to define the module T_FF inside
// this module.
module ripple_carry_counter(q, clk, reset);
output [3:0] q;
input clk, reset;
module T_FF(q, clock, reset);// ILLEGAL MODULE NESTING
:
<module T_FF internals>
:
endmodule // END OF ILLEGAL MODULE NESTING
endmodule

## Slide 21: Gates
Basic element for designing a digital logic circuit
Verilog supports basis logic gates as predefined primitives
  installed like modules
  predefined in Verilog (do not need a module definition)
  Basic Gates:
    and/or : one scalar output and multiple scalar inputs
    buf/not : one scalar input and one or more scalar outputs
  Other predefined gates: xor, nand, nor, xnor

## Slide 22: Ports
Ports provide the interface by which a module can communicate with its environment
  input/output pins of an IC chip are its ports
A module definition contains an optional list of ports
If the module does not exchange any signals with the environment, there are no ports in the list

## Slide 23: Ports (cont.)
module fulladd4(sum, c_out, a, b, c_in);
module Top
Full adder
(4-bit)
fulladd4
a
b
cin
cout
sum
Top

## Slide 24: Ports (cont.)
Port Declaration
  input : Input port
  Output : Output port
  inout : Bidirectional port
module fulladd4(sum, c_out, a, b, c_in);
//begin port declarations section
  output [3:0] sum;
  output c_out;
  input [3:0] a, b;
  input c_in;
//end port declaration section
  .......
  <module internals>
  .......
endmodule;

## Slide 25: Ports (cont.)
    Port Connection Rules
net inout
net
reg or net
net
input
net
output
reg or net

## Slide 26: Verilog Value Set
0 represents low logic level or false condition
1 represents high logic level or true condition
x represents unknown logic level
z represents high impedance logic level

## Slide 27: Numbers in Verilog (i)
<size>’<radix> <value>
  8’h ax = 1010xxxx
  12’o 3zx7 = 011zzzxxx111
No of
bits
Binary  b or B
Octal  o or O
Decimal  d or D
Hexadecimal  h or H
Consecutive chars
0-f, x, z

## Slide 28: Numbers in Verilog (ii)
You can insert “_” for readability
  12’b 000_111_010_100
  12’b 000111010100
  12’o 07_24
Bit extension
  MS bit = 0, x or z  extend this
    4’b x1 = 4’b xx_x1
  MS bit = 1  zero extension
    4’b 1x = 4’b 00_1x
Represent the same number

## Slide 29: Numbers in Verilog (iii)
If size is ommitted it
  is inferred from the value or
  takes the simulation specific number of bits or
  takes the machine specific number of bits
If radix is ommitted too .. decimal is assumed
  15 = <size>’d 15

## Slide 30: Nets (i)
Can be thought as hardware wires driven by logic
Equal z when unconnected
Various types of nets
  wire
  wand (wired-AND)
  wor (wired-OR)
  tri (tri-state)
In following examples: Y is evaluated, automatically, every time A or B changes

## Slide 31: Nets (ii)
A
B
Y
wire Y; // declaration
assign Y = A & B;
B
A
Y
wand Y; // declaration
assign Y = A;
assign Y = B;
wor Y; // declaration
assign Y = A;
assign Y = B;
A
Y
dr
tri Y; // declaration
assign Y = (dr) ? A : z;

## Slide 32: Registers
Variables that store values
Do not represent real hardware but ..
.. real hardware can be implemented with registers
Only one type: reg
  reg A, C; // declaration
  // assignments are always done inside a procedure
  A = 1;
  C = A; // C gets the logical value 1
  A = 0; // C is still 1
  C = 0; // C is now 0
Register values are updated explicitly!!

## Slide 33: Vectors
Represent buses
  wire [3:0] busA;
  reg [1:4] busB;
  reg [1:0] busC;
Left number is MS bit
Slice management
  busC[1] = busA[2];
  busC[0] = busA[1];
Vector assignment (by position!!)
busB[1] = busA[3];
  busB[2] = busA[2];
  busB[3] = busA[1];
  busB[4] = busA[0];
busB = busA; 
busC = busA[2:1]; 

## Slide 34: Integer & Real Data Types
Declaration
  integer i, k;
  real r;
Use as registers (inside procedures)
  i = 1; // assignments occur inside procedure
  r = 2.9;
  k = r; // k is rounded to 3
Integers are not initialized!!
Reals are initialized to 0.0

## Slide 35: Time Data Type
Special data type for simulation time measuring
Declaration
  time my_time;
Use inside procedure
  my_time = $time; // get current sim time
Simulation runs at simulation time, not real time

## Slide 36: Arrays (i)
Syntax
  integer count[1:5]; // 5 integers
  reg var[-15:16]; // 32 1-bit regs
  reg [7:0] mem[0:1023]; // 1024 8-bit regs
Accessing array elements
  Entire element: mem[10] = 8’b 10101010;
  Element subfield (needs temp storage):
    reg [7:0] temp;
    ..
    temp = mem[10];
    var[6] = temp[2];

## Slide 37: Arrays (ii)
Limitation: Cannot access array subfield or entire array at once
  var[2:9] = ???; // WRONG!!
  var = ???; // WRONG!!
No multi-dimentional arrays
  reg var[1:10] [1:100]; // WRONG!!
Arrays don’t work for the Real data type
  real r[1:10]; // WRONG !!

## Slide 38: Strings
Implemented with regs:
  reg [8*13:1] string_val; // can hold up to 13 chars
  ..
  string_val = “Hello Verilog”;
  string_val = “hello”; // MS Bytes are filled with 0
  string_val = “I am overflowed”; // “I ” is truncated
Escaped chars:
  \n newline
  \t tab
  %% %
  \\ \
  \“ “

## Slide 39: Logical Operators
&&  logical AND
||  logical OR
!  logical NOT
Operands evaluated to ONE bit value: 0, 1 or x
Result is ONE bit value: 0, 1 or x
  A = 6; A && B  1 && 0  0
  B = 0; A || !B  1 || 1  1
  C = x; C || B  x || 0  x
but C && B = 0

## Slide 40: Bitwise Operators (i)
&  bitwise AND
|  bitwise OR
~  bitwise NOT
^  bitwise XOR
~^ or ^~  bitwise XNOR
Operation on bit by bit basis

## Slide 41: Bitwise Operators (ii)
c = ~a;
c = a & b;
a = 4’b1010;
b = 4’b1100;
a = 4’b1010;
b = 2’b11;
c = a ^ b;

## Slide 42: Reduction Operators
&  AND
|  OR
^  XOR
~&  NAND
~|  NOR
~^ or ^~  XNOR
One multi-bit operand  One single-bit result
  a = 4’b1001;
  ..
  c = |a; // c = 1|0|0|1 = 1

## Slide 43: Shift Operators
>>  shift right
<<  shift left
Result is same size as first operand, always zero filled
a = 4’b1010;
...
d = a >> 2; // d = 0010
c = a << 1; // c = 0100

## Slide 44: Concatenation Operator
{op1, op2, ..}  concatenates op1, op2, .. to single number
Operands must be sized !!
  reg a;
  reg [2:0] b, c;
  ..
  a = 1’b 1;
  b = 3’b 010;
  c = 3’b 101;
  catx = {a, b, c}; // catx = 1_010_101
  caty = {b, 2’b11, a}; // caty = 010_11_1
  catz = {b, 1}; // WRONG !!
Replication ..
  catr = {4{a}, b, 2{c}}; // catr = 1111_010_101101

## Slide 45: Relational Operators
>  greater than
<  less than
>=  greater or equal than
<=  less or equal than
Result is one bit value: 0, 1 or x
  1 > 0  1
  ’b1x1 <= 0  x
  10 < z  x

## Slide 46: Equality Operators
==  logical equality
!=  logical inequality
===  case equality
!==  case inequality
  4’b 1z0x == 4’b 1z0x  x
  4’b 1z0x != 4’b 1z0x  x
  4’b 1z0x === 4’b 1z0x  1
  4’b 1z0x !== 4’b 1z0x  0
Return 0, 1 or x
Return 0 or 1

## Slide 47: Conditional Operator
cond_expr ? true_expr : false_expr
Like a 2-to-1 mux ..
A
B
Y
sel
Y = (sel)? A : B;
0
1

## Slide 48: Arithmetic Operators (i)
+, -, *, /, %
If any operand is x the result is x
Negative registers:
  regs can be assigned negative but are treated as unsigned
    reg [15:0] regA;
    ..
    regA = -4’d12; // stored as 216-12 = 65524
    regA/3 evaluates to 21861

## Slide 49: Arithmetic Operators (ii)
Negative integers:
  can be assigned negative values
  different treatment depending on base specification or not
    reg [15:0] regA;
    integer intA;
    ..
    intA = -12/3; // evaluates to -4 (no base spec)
    intA = -’d12/3; // evaluates to 1431655761 (base spec)

## Slide 50: Operator Precedence
Use parentheses to
enforce your
priority

## Slide 51: Simulation- Test Bench Styles

## Slide 52: Example
Design block was shown before
  ripple_carry_counter, T_FF, and D_FF modules
Stimulus block

## Slide 53: Example (cont’d)
module stimulus;
reg clk; reg reset; wire[3:0] q;
// instantiate the design block
ripple_carry_counter r1(q, clk, reset);
// Control the clk signal that drives the design block.
initial clk = 1'b0;
always #5 clk = ~clk;
// Control the reset signal that drives the design block
initial
begin
reset = 1'b1;
#15 reset = 1'b0;
#180 reset = 1'b1;
#10 reset = 1'b0;
#20 $stop;
end
initial // Monitor the outputs
$monitor($time, " Output q = %d", q);
endmodule